Streamline Ink Conversion

I have detailed below an outline guide to the two procedures:

OEM inks to Streamline

Sun Chemical Streamline inks have been formulated to be chemically miscible and colour compatible with the OEM ink. This will allow the operator to replace the empty OEM ink cartridge with the Streamline product as required. No flushing of the ink circuit is required. Your local sales agent should obtain a nozzle pattern test and printer health check before the Sun Chemical inks are installed on the printer.

Sun Chemical only guarantees Streamline inks for use with a compatible OEM ink. Please check with your local agent before selecting your product.

Non – OEM inks to Streamline

Sun Chemical Streamline inks have not been formulated for compatibility with non-original inks. The change from non-OEM inks to Sun chemical Streamline should be performed by a qualified engineer. The engineer will follow the following procedure:

- Before conversion – perform nozzle pattern test, print test file and carry out printer health check (visual inspection)

- Remove existing cartridges or bulk tank system*

- Install Sun Chemical flushing cartridges in each slot

- Prime system with flushing fluid and pump all ink supply tubes until clear

- Install Sun Chemical Streamline cartridges or bulk tank system

- Prime system until all ink tubes are filled, purge and prime print heads

- Perform nozzle pattern test and print test file

On completion the engineer will compare results. If any nozzles are missing that were present before the ink conversion, the engineer will perform several head cleans until the nozzles are restored.

Sun Chemical does not recommend re-use of bulk tank systems that have previously contained non-OEM ink. Flexible options are available for replacement with a Sun Chemical approved system.

The Sun Chemical Warrantee will be invalid for ink conversions that have not observed the recommended procedure.